## Slide 1
Extremely
Time-consuming
Project
Presentation
2023.5.15
朱宇轩 赵子豪

## Slide 2
Content
Fiber Optic Communication
APD Area Review
Paper Reproduction

## Slide 3
Content
APD Area Review
Noise and Main parameters
In0.53Ga0.47As
SACM APD
Ge/Si APD
Reduce the thickness of the multiplier layer
In0.52Al0.48As
Three mesa
Two-layer absorption
Impact Ionization Engineering
Longer wavelength

## Slide 4
Content
Paper Reproduction
Determination of basic parameters
Electrical field
Workmanship
Ohmic contact
Graded band
Initial value
Simulation attempt
N17
P3
N18
Dual Charge Layers
Theoretical analysis
P15
P13
Three mesa
Structure B comparison
Structure C comparison
Reliability
Unintentional doping
Gradient problem
Current dependent
Dark current
Light current

## Slide 5
Fiber Optic
Fiber Optic Communication

## Slide 6
Fiber Optic
Reducing loss

## Slide 7
Silicon Dioxide
SiO2 absorption
optical transparency
mechanical strength
electromagnetic interference resistance
cost-effectiveness

## Slide 8
Silicon Dioxide
vibration mode of the Si-O bond network
bonding electrons
SiO2 light absorption

## Slide 9
Silicon Dioxide
[1] https://www.sohu.com/a/580776421_120733531
Scattering
Rayleigh scattering
spontaneous Raman scattering
brillouin scattering
high light intensity
short-wavelength

## Slide 10
Water Vapor
water vapor light absorption
[1] Carter, G.A. (1993). "Relationship of leaf spectral reflectance to chloroplast water content determined using NMR microscopy". Remote Sensing of Environment. 46 (3): 305–310.
[2] Rossel, R.A.V. (1998). "Laboratory evaluation of a proximal sensing technique for simultaneous measurement of soil clay and water content". Geoderma. 85 (1): 19–39.

## Slide 11
Content
APD Area Review
Noise and Main parameters
In0.53Ga0.47As
SACM APD
Ge/Si APD
Reduce the thickness of the multiplier layer
In0.52Al0.48As
Three mesa
Two-layer absorption
Impact Ionization Engineering
Longer wavelength

## Slide 12
APD

## Slide 13
Performance Index
Thermal noise
Noise
Particle noise
Gain
Core Index
Excess noise factor
Gain-bandwidth product
Bandwidth

## Slide 14
In0.53Ga0.47As
Bandgap: 0.79eV
Advantage
Lattice constant: 5.868Å
matching well with InP
[4] Cook, L. W. Electron and hole impact ionization coefficients in InP determined by photomultiplication measurements[J]. Applied Physics Letters, 1982, 40(7): 589-591.

## Slide 15
InP
InP
Low dark current
Pure hole carrier
Low noise

## Slide 16
SACM APD
relatively weak absorption efficiency
an absorption layer of at least 2.5 μm
longer transition time
lower Gain–bandwidth product

## Slide 17
SACM APD
Disadvantage
low Gain–bandwidth product
Produce more noise than Si
Cannot be integrated with the silicon based CMOS process
Expensive
Poor crystal quality
Complex manufacturing process

## Slide 18
Ge/Si
Wavelength is calculated to be 1.1 μm
Si
Lattice mismatch
Low absorption efficiency near the cutoff wavelength
Ge
Absorption region
Multiplication region
[5] Shah V A, et al. Effect of layer thickness on structural quality of Ge epilayers grown directly on Si(001)[J]. Thin Solid Films, 2011, 519(22): 7911-7917.

## Slide 19
Lattice Mismatch
Lattice mismatch
Rough surface of Ge
High density of dislocation defects
Dark current
Noise
Power consumption
[6] Masini G, et al. High responsitivity near infrared Ge photodetectors integrated on Si[J]. Electronics Letters, 1999, 35(17): 1467-1468.
[7] Wei Y, et al. Analysis of dark current dependent upon threading dislocations in Ge/Si heterojunction photodetectors[J]. Microelectronics International, 2012, 29(3): 136-140.

## Slide 20
Multiplication layer thickness

## Slide 21
In0.52Al0.48As
bandgap 1.437 eV
matching lattice constant
Replace InP
As multiplication layer
Reduce noise

## Slide 22
Three mesa
avoiding the need for a guard ring
reduces the electric field at the edges
preventing edge breakdown and surface current leakage
high electric field region is limited to the space directly below the top surface

## Slide 23
Two absorption region
partially depleted p+
i-type depleted
Increasing electric field
Enlarging gain
Increasing absorption efficiency

## Slide 24
Two absorption region
[8] Alpha, M. & Daniel, Thomas. (2015). Effect of Doping Concentration on the Electrical and Optical Properties of Zn: SnO 2. IOSR Journal of Applied Physics. 7. 38-44. 10.9790/4861-07323844..
[9] Dakhlaoui, H. (2012) Effect of the Doping Layer Concentration on Optical Absorption in Si δ-Doped GaAs Layer. Optics and Photonics Journal, 2, 140-144. doi: 10.4236/opj.2012.23020.

## Slide 25
Impact Ionization Engineering
Enhance higher-ionization-rate carrier collision ionization
Cascade low-noise gain regions
I2E
Materials with smaller bandgap width

## Slide 26
Bigger Wavelength
Capacity crunch
Increasing the bandwidth of optical fiber transmission system
More data can be transmitted on same infrastructure

## Slide 27
Bigger Wavelength
WDM
(Wavelength Division Multiplexing)
Higher transmission capacity
Improving data transmission efficiency

## Slide 28
Content
Paper Reproduction
Determination of basic parameters
Electric field
Workmanship
Ohmic contact
Graded band
Initial value
Simulation attempt
N17
P3
N18
Dual Charge Layers
Theoretical analysis
P15
P13
Three mesa
Structure B comparison
Structure C comparison
Reliability
Unintentional doping
Gradient problem
Current dependent
Dark current
Light current

## Slide 29
Electrical field
[10] M. Littlejohn, K. Kim, and H. Tian, ``High-Field Transport in InGaAs and Related Heterostructures,'' in Bhattacharya, section 4.2, pp. 107-116.
In0.52Al0.48As

## Slide 30
Workmanship

## Slide 31
Ohmic Contact

## Slide 32
Graded Band
Material | Wavelength(um)
In0.61Al0.04Ga0.35As | 1
In0.58Al0.03Ga0.39As | 1.2
In0.55Al0.06Ga0.39As | 1.4
In0.52Al0.12Ga0.36As | 1.6

## Slide 33
Graded Band
Material | Wavelength(um)
In0.2Al0.500Ga0.300As | 1
In0.2Al0.367Ga0.433As | 1.2
In0.2Al0.234Ga0.566As | 1.4
In0.2Al0.100Ga0.700As | 1.6

## Slide 34
Discontinuity of Eg

## Slide 35
Continuity of Eg

## Slide 36
Initial Value

## Slide 37
Initial Value
0.9Vbr_-21V:
1052.6 kV/cm
Punch_-8V:
779.88 kV/cm

## Slide 38
Initial Value
612.10 kV/cm

## Slide 39
Chart: Influence of n17 on Electrical Filed
| 1E+18 | 3E+18 | 5E+18 | 7E+18 | 9E+18 | 1E+19 | 3E+19 | 5E+19
Center | 1001.1 | 1038.1 | 1046.2 | 1049.8 | 1051.8 | 1052.6 | 1057.1 | 1058.1
Margin | 610.14 | 611.62 | 612.02 | 611.98 | 612.18 | 612.12 | 612.4 | 612.52
n17 | 1.00E+18 | 3.00E+18 | 5.00E+18 | 7.00E+18 | 9.00E+18 | 1.00E+19 | 3.00E+19 | 5.00E+19
Center | 1001.1 | 1038.1 | 1046.2 | 1049.8 | 1051.8 | 1052.6 | 1057.1 | 1058.1
Margin | 610.14 | 611.62 | 612.02 | 611.98 | 612.18 | 612.12 | 612.4 | 612.52
n17

## Slide 40
Chart: Influence of p3 on Electrical Filed
| 100000000000000 | 1000000000000000 | 1E+16 | 2E+16 | 4E+16 | 6E+16 | 8E+16 | 1E+17 | 1E+18 | 1E+19
Center | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6
Margin | 612.16 | 612.18 | 612.2 | 612.22 | 612.14 | 612.26 | 612.2 | 612.12 | 612.18 | 612.24
p3 | 1.00E+14 | 1.00E+15 | 1.00E+16 | 2.00E+16 | 4.00E+16 | 6.00E+16 | 8.00E+16 | 1.00E+17 | 1.00E+18 | 1.00E+19
Center | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6
Margin | 612.16 | 612.18 | 612.2 | 612.22 | 612.14 | 612.26 | 612.2 | 612.12 | 612.18 | 612.24
p3

## Slide 41
n18 | 1.00E+14 | 1.00E+15 | 1.00E+16 | 1.00E+17 | 1.00E+18 | 1.00E+19
Center | 1052.6 | 1052.6 | 1.05E+03 | 1.05E+03 | 1052.6 | 1052.6
Margin | 612.21 | 612.12 | 612.24 | 612.03 | 612.24 | 612.14
Chart: Influence of n18 on Electrical Filed
| 100000000000000 | 1000000000000000 | 1E+16 | 1E+17 | 1E+18 | 1E+19
Center | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6
Margin | 612.21 | 612.12 | 612.24 | 612.03 | 612.24 | 612.14
n18

## Slide 42
Dual charge layer

## Slide 43
Dual charge layer

## Slide 44
p15 | 1.00E+18 | 1.50E+18 | 2.00E+18 | 2.50E+18
Center | 873.6 | 1052.6 | 1.23E+03 | 1407.8
Margin | 416.6 | 612.22 | 807.62 | 1003.1
Chart: Influence of p15 on Electrical Filed
| 1E+18 | 1.5E+18 | 2E+18 | 2.5E+18
Center | 873.6 | 1052.6 | 1230.7 | 1407.8
Margin | 416.6 | 612.22 | 807.62 | 1003.1
p15

## Slide 45
p13 | 3.50E+17 | 4.00E+17 | 4.50E+17 | 5.00E+17 | 5.50E+17 | 6.00E+17 | 6.50E+17 | 7.00E+17 | 7.50E+17 | 8.00E+17
Center | 1008.3 | 1023.1 | 1037.8 | 1052.6 | 1067.3 | 1081.9 | 1096.6 | 1111.2 | 1125.8 | 1140.4
Margin | 612.1 | 612.2 | 612.05 | 611.97 | 612.1 | 612.2 | 612.12 | 612.16 | 612.12 | 612.2
Chart: Influence of p13 on Electrical Filed
| 3.5E+17 | 4E+17 | 4.5E+17 | 5E+17 | 5.5E+17 | 6E+17 | 6.5E+17 | 7E+17 | 7.5E+17 | 8E+17
Center | 1008.3 | 1023.1 | 1037.8 | 1052.6 | 1067.3 | 1081.9 | 1096.6 | 1111.2 | 1125.8 | 1140.4
Margin | 612.1 | 612.2 | 612.05 | 611.97 | 612.1 | 612.2 | 612.12 | 612.16 | 612.12 | 612.2
p13

## Slide 46
Structure B comparison

## Slide 47
1052.4kV/cm
837.68kV/cm
Structure B comparison

## Slide 48
Structure C comparison

## Slide 49
64kV/cm
165.78kV/cm
Structure C comparison

## Slide 50
629.04kV/cm
1052.4kV/cm
Structure C comparison

## Slide 51
i | 1.00E+10 | 1.00E+11 | 1.00E+12 | 1.00E+13 | 1.00E+14 | 1.00E+15
Center | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1051.8
Margin | 612.16 | 612.11 | 612.26 | 612.22 | 612.56 | 613.72
Chart: Influence of i on Electrical Filed
| 10000000000 | 100000000000 | 1000000000000 | 10000000000000 | 100000000000000 | 1000000000000000
Center | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1052.6 | 1051.8
Margin | 612.16 | 612.11 | 612.26 | 612.22 | 612.56 | 613.72
i

## Slide 52
Chart: Influence of doping grade on Electrical Filed
| linear | exp | square
Center | 1063.3 | 1052.6 | 1064
Margin | 612.23 | 612.12 | 612.34
Graded doping type

## Slide 53
Dark Current
Current
Light Current